## Slide 1: Project documentation for supercross_learner
Table of contents:
Background info and motivation
Description of environment physics
Description of tracks
Environment validation
Description of .py file interaction
Progress of the learner
TODO and ideas for improvement

## Slide 2
Background and Motivation:
RedBull Moto 8 movie “supercross is like a game of chess” alluding to the strategic part of jumping relative to your opponent.
  If we can teach a computer to play chess, then can we teach a compute to race supercross.
Kawasaki “Science of Supercross” episodes describe some techniques of the strategy of supercross.
  on/off - episode 8
  scrub - episode 12, but this needs many DOFs. greater take off speed, less height, less time in air, same size jump.
  Jump timing. episode 23. Backside, in the flat, on the face, Hang the back wheel.
  rhythm section, ep34. double, triple, quad, on/off combinations

## Slide 3
Free body diagrams for environment model (supercross_env). The bike model has only one wheel. There is only 1 DOF between wheel and bike.
The wheel does have a “magic formula” style slip vs grip behavior.
theta
Fn
-Fs
Ft
wheel
bike
Fs
-Fg
-Fdragx
-Fdragy
Bike Free Body
Mb*axb = -Fdragx + whlFx
Mb*ayb = -Fdragy - Fg + Fs
Wheel Free Body
If inAir
Fn=Ft=whlFx=0
whlFy =(-Fg-Fs)
Else
Fn=(-Fg-Fs)*cos(theta)
Ft=min(trq/whlRad,Fn*nu)+(-Fg-Fs)*sin(theta)
whlFx = -Fn*sin(theta)+Ft*cos(theta)
whlFy = Fn*cos(theta)+Ft*sin(theta)
Axw=axb, there is no x-dir DOF between wheel and bike
Mw*ayw = whlFym but this is irrelevant since wheel ayw is a function of following track profile.
-Fg

## Slide 4
Describe (supercross_track_maker). The track maker feeds track profiles to supercross_env. Track profiles are 2D, viewed from the side. The track maker makes track features: flats, triple jumps, table tops, on/offs, whoops, etc, it then combines these features in either pre-ordered sequences, or random sequences to make tracks of specific length.
This could be improved, but the code does a pretty good job, so look there if this is inadequate.

## Slide 5
Environment validation. Is the environment realistic relative to a real supercross bike and track?
Distance (meters)
Speed(m/s)
Testing data obtained from internet.
Comparison between test data and model
(no learning agent, full throttle input to environment).
Speed(m/s)
Time (s)

## Slide 6
10% and 10x
30% and 10x
50% and 10x
30% and 5x
Selected by visual inspection
Exploring the behavior of progressive suspension stiffness.
As suspension nears bottoming, ramp up stiffness [1x -> ?x] as travel goes [?% -> 100%]

## Slide 7: Description of .py file interaction NOT DONE

## Slide 8: Section for progress of the learner

## Slide 9: First success with tensorForce
Uses default PPO agent from OpenAI gym Cart Pole example.
Env is just the track with single triple jump (i.e. mk_trk1()). Plot show throttle and bike X position vs time.
We can see the trend towards more full throttle, not rolling backwards on jump face. Still some ambiguity with what to do at start. Obviously because it only see 30m ahead, and 30m ahead of start there is nothing. But what's nice about that is we see that as soon as it does see a feature like jump face, high throttle actions predominate.
Reward at ep3000=3.4
Best reward =4.1
Worst reward = approx. -1e6

## Slide 10: First success with tensorForce
Uses default PPO agent from OpenAI gym Cart Pole example.
Env is just the track with single triple jump (i.e. mk_trk1()). Plot show throttle and bike X position vs time.
We can see the trend towards more full throttle, shorter episode time, and monotonic Xpos increase over episode (i.e. no rolling back down jump face)
Reward at ep3000=3.4
Best reward =4.1
Worst reward = approx. -1e6

## Slide 11
Shortened mk_trk1 starting flat section to be closer to agent look ahead distance, and this might be the cause of the almost no learning for that test
Order of figures: Ep3000ep1
Why is this? I think it could be because learning is a stochastic process, due the random element of the explore/exploit process, which means running the same experiment twice will not result in the same learning rate. So maybe this was just a bad experiment in terms of global learning rate (i.e. how much better agent gets over 300 episodes).

## Slide 12
Mk_trk1 in run = 120ft
Order of figures: Ep1->ep3000
Here, global learning rate was slower than for the test on slides 6 & 7
Continue training after stop at ep3000, to ep6000
We can see that here it took about 3500 episodes to achieve similar performance as we saw after only 2000 episodes on slides 6 & 7
Finished episode 2986 after 134 timesteps (reward: -3.2999999999999687)
Finished episode 2987 after 91 timesteps (reward: 1.000000000000016)
Finished episode 2988 after 109 timesteps (reward: -0.7999999999999776)
Finished episode 2989 after 122 timesteps (reward: -2.099999999999973)
Finished episode 2990 after 100 timesteps (reward: 0.10000000000001918)
Finished episode 2991 after 108 timesteps (reward: -0.699999999999978)
Finished episode 2992 after 104 timesteps (reward: -0.2999999999999794)
Finished episode 2993 after 106 timesteps (reward: -0.4999999999999787)
Finished episode 2994 after 184 timesteps (reward: -8.29999999999999)
Finished episode 2995 after 164 timesteps (reward: -6.299999999999962)
Finished episode 2996 after 96 timesteps (reward: 0.5000000000000178)
Finished episode 2997 after 122 timesteps (reward: -2.099999999999973)
Finished episode 2998 after 96 timesteps (reward: 0.5000000000000178)
Finished episode 2999 after 119 timesteps (reward: -1.799999999999974)
Finished episode 3000 after 140 timesteps (reward: -3.8999999999999666)
INFO:tensorflow:Saving checkpoints for 632416 into ./savedTest02/model.ckpt.
Learning finished. Total episodes: 3000. Average reward of last 10 episodes: -2.289999999999977.
cummulative execution time: 3585.5566997528076
Finished episode 5985 after 58 timesteps (reward: 4.300000000000004)
Finished episode 5986 after 59 timesteps (reward: 4.200000000000005)
Finished episode 5987 after 58 timesteps (reward: 4.300000000000004)
Finished episode 5988 after 58 timesteps (reward: 4.300000000000004)
Finished episode 5989 after 59 timesteps (reward: 4.200000000000005)
Finished episode 5990 after 59 timesteps (reward: 4.200000000000005)
Finished episode 5991 after 58 timesteps (reward: 4.300000000000004)
Finished episode 5992 after 58 timesteps (reward: 4.300000000000004)
Finished episode 5993 after 59 timesteps (reward: 4.200000000000005)
Finished episode 5994 after 59 timesteps (reward: 4.200000000000005)
Finished episode 5995 after 59 timesteps (reward: 4.200000000000005)
Finished episode 5996 after 58 timesteps (reward: 4.300000000000004)
Finished episode 5997 after 58 timesteps (reward: 4.300000000000004)
Finished episode 5998 after 58 timesteps (reward: 4.300000000000004)
Finished episode 5999 after 57 timesteps (reward: 4.400000000000004)
Finished episode 6000 after 57 timesteps (reward: 4.400000000000004)
INFO:tensorflow:Saving checkpoints for 858269 into ./savedTest02/model.ckpt.
Learning finished. Total episodes: 6000. Average reward of last 10 episodes: 4.2900000000000045.
cummulative execution time: 1252.185539007187

## Slide 14
TODO:
Environment:
Create random track generator
  This should have a target total length argument. I think it will be important to have tracks not be too long at first, but as the agent gets better, then tracks can get longer without risk of losing the necessary rewards signal.
Create whoops section feature
The rewards are “working”, but are not necessarily what we want. Some places to improve:
  As the agent gets better, and tracks get longer, eventually the difference between a fast race and slow race will be small fractions of total time it takes to complete the whole race. As such, we want to amplify the “betterness” of a race that takes just a tiny fraction less time than another, which means a “win” in the context of racing. So maybe keep track of the best time so far, and then once the time for the present race is longer, scale the per step rewards to be a larger negative reward?
  Does the +10 at the terminal state make sense? I think that, if this is only awarded when the race time is shorter than the best, this could be a ok way to provide a strong rewards signal for doing “just a bit better”.
Solver performance
  Check Momentum conservation across change in direction at jump face transition.
  Variable step solver? As bike or wheel acceleration in either X or Y direction goes from [lwr_thr -> upr_thr], time steps goes [dt -> dt/n], where n is positive integer. Still only record data every dt, so run sub-loops at dt/n until a dt size step is complete, then record data
State ideas: Thinking about what mental model a rider would have for the track, these are some state ideas that could work well.
Include a vector which maps out the track features. E.g. 00102040100203, some flat, some flat, a table top, some flat, a double triple jump, some flat, some whoops, etc. this vector encodes the track layout for the agent, so the agent can plan its strategy. A rider would not commit a high fidelity layout to memory, but surely would be able to tell someone the sequence of features from memory.
Have the track profile portion of the state vector be variable length. A minimum length, but if there is a long flat section, the resolution would drop, so seeing further in distance space with same number of sample points. This would help the agent start moving at the beginning for tracks that have a start section that is flat for longer distance than the minimum length. This is sort of attune to how humans look ahead, the more features there are ahead, the less far we look, if there are few or no feature in the near distance, we sort of turn our focus away from that, and look far ahead, with poor resolution, to see what features we can.
Agent and hyper parameters
Setup multi-treading
Setup Bayesian optimization
Model architecture
  Add drop out. Will this be helpful in this context?