## Slide 1
Free body diagrams for environment model. The bike model has only one wheel. There is only 1 DOF between wheel and bike.
theta
Fn
-Fs
Ft
wheel
bike
Fs
-Fg
-Fdragx
-Fdragy
Bike Free Body
Mb*axb = -Fdragx + whlFx
Mb*ayb = -Fdragy - Fg + Fs
Wheel Free Body
If inAir
Fn=Ft=whlFx=0
whlFy =(-Fg-Fs)
Else
Fn=(-Fg-Fs)*cos(theta)
Ft=min(trq/whlRad,Fn*nu)+(-Fg-Fs)*sin(theta)
whlFx = -Fn*sin(theta)+Ft*cos(theta)
whlFy = Fn*cos(theta)+Ft*sin(theta)
Axw=axb, there is no x-dir DOF between wheel and bike
Mw*ayw = whlFym but this is irrelevant since wheel ayw is a function of following track profile.
-Fg

## Slide 4
Check Momentum conservation across change in direction at jump face transition.
Variable step solver? As bike or wheel acceleration in either X or Y direction goes from [lwr_thr -> upr_thr], time steps goes [dt -> dt/n], where n is positive integer. Still only record data every dt, so run sub-loops at dt/n until a dt size step is complete, then record data

## Slide 5
10% and 10x
30% and 10x
50% and 10x
30% and 5x
Selected by visual inspection
Suspension bottoming, ramp up stiffness [1x -> ?x] as travel goes [?% -> 100%]

## Slide 6: First success with tensorForce
Uses default PPO agent from OpenAI gym Cart Pole example.
Env is just the track with single triple jump (i.e. mk_trk1()). Plot show throttle and bike X position vs time.
We can see the trend towards more full throttle, not rolling backwards on jump face. Still some ambiguity with what to do at start. Obviously because it only see 30m ahead, and 30m ahead of start there is nothing. But what's nice about that is we see that as soon as it does see a feature like jump face, high throttle actions predominate.
Reward at ep3000=3.4
Best reward =4.1
Worst reward = approx. -1e6

## Slide 7: First success with tensorForce
Uses default PPO agent from OpenAI gym Cart Pole example.
Env is just the track with single triple jump (i.e. mk_trk1()). Plot show throttle and bike X position vs time.
We can see the trend towards more full throttle, shorter episode time, and monotonic Xpos increase over episode (i.e. no rolling back down jump face)
Reward at ep3000=3.4
Best reward =4.1
Worst reward = approx. -1e6