## Slide 1: Project documentation for supercross_learner
This is a project with the goal of teaching an AI agent to race a supercross bike on a track similar to a Red Bull straight rhythm track. The goal is to have the agent learn how to strategize about jump timing, throttle control over a range of track features, etc. so as to complete the track distance within as short a time as possible. The name supercross_learner came from AMA supercross, which is similar to straight rhythm, but has corners. So the agent is learning the aspects of supercross that are prevalent in the straight rhythm competition, with the modeling advantage of reduced complexity from omitting corners.
Table of contents:
Background info and motivation
Description of environment physics
Description of tracks
Environment validation
Description of .py file interaction
Progress of the learner
TODO and ideas for improvement

## Slide 2
Background and Motivation:
RedBull Moto 8 movie narrator “supercross is like a game of chess” alluding to the strategic part of jumping relative to your opponent.
  If we can teach a computer to play chess, then can we teach a compute to race supercross.
Kawasaki “Science of Supercross” episodes describe some techniques of the strategy of supercross.
  on/off - episode 8
  scrub - episode 12, but this needs many DOFs. greater take off speed, less height, less time in air, same size jump.
  Jump timing - episode 23. Backside, in the flat, on the face, Hang the back wheel.
  rhythm section – episode 34. double, triple, quad, on/off combinations
Why make my own environment?
  Was not aware of a 2D motocross/supercross game that had realistic track profiles (features types, approach radii, landing radii, etc.), and realistic bike performance (suspension behavior, power and drag characteristics, etc.).
  Did not want a degree of freedom allowing the bike+wheel body to rotate.
  3D moto/supercross games offer too many degrees of freedom for this initial work.
  It was a good learning experience, and it was fun.

## Slide 3
Free body diagrams for environment model (supercross_env). The bike model has only one wheel. There is only 1 DOF between wheel and bike.
The wheel does not have “magic formula” style slip vs grip behavior. There is not DOF for wheel rotation, wheel rotation is relative to ground speed. There is however, grip as a function of normal force, so if wheel normal force is low, not all torque will result in bike acceleration.
theta
Fn
-Fs
Ft
wheel
bike
Fs
-Fg
-Fdragx
-Fdragy
Bike Free Body
Mb*axb = -Fdragx + whlFx
Mb*ayb = -Fdragy - Fg + Fs
Wheel Free Body
If inAir
Fn=Ft=whlFx=0
whlFy =(-Fg-Fs)
Else
Fn=(-Fg-Fs)*cos(theta)
Ft=min(trq/whlRad,Fn*nu)+(-Fg-Fs)*sin(theta)
whlFx = -Fn*sin(theta)+Ft*cos(theta)
whlFy = Fn*cos(theta)+Ft*sin(theta)
Axw=axb, there is no x-dir DOF between wheel and bike
Mw*ayw = whlFym but this is irrelevant since wheel ayw is a function of following track profile.
-Fg

## Slide 4
Describe (supercross_track_maker). The track maker feeds track profiles to supercross_env. Track profiles are 2D, viewed from the side. The track maker makes track features: flats, triple jumps, table tops, on/offs, whoops, etc, it then combines these features in either pre-ordered sequences, or random sequences to make tracks of specific length.
Example of randomly ordered set of flat, table top, on/off, and triple jump. Units here are in meters
Zoom into to a triple jump to see the details of the profile curves, joint, and non-curved sections: units here are feet.
Note, due to the natural aspect ratio of these tracks and features, they are very hard to show with equal X-Y scaling, and fit them on a compute screen. So note that Y axis is always over magnified.

## Slide 5: Environment validation
Table of contents:
Power and drag characteristics
Jumping and suspension behavior
Drop test (not yet shown)

## Slide 6
Environment validation. Is the environment realistic relative to a real supercross bike and track?
Distance (meters)
Speed(m/s)
Testing data obtained from internet.
Comparison between test data and model
(no learning agent, full throttle input to environment).
Speed(m/s)
Time (s)

## Slide 7
10% and 10x
30% and 10x
50% and 10x
30% and 5x
Selected by visual inspection
Exploring the behavior of progressive suspension stiffness.
As suspension nears bottoming, ramp up stiffness [1x -> ?x] as travel goes [?% -> 100%]

## Slide 8
Exploring the behavior of suspension when dropping the bike. Units in meters.
bkY=vertical position of bike CG
whlY=vertical position of wheel CG, which is wheel center. Note minimum of 0.3m off ground, 0.3m=wheel radius
inAir=Boolean indicating whether wheel is in contact with ground or not.
sTY=suspension travel. Convention 0=fully compressed, 0.3 = fully extended.

## Slide 9: Description of .py file interaction NOT DONE

## Slide 10: Section for progress of the learner

## Slide 11: SubSection for progress of the learner with this neural net. Name=net03
32
32
Input layer:
# state is vector concatenated of vectors and scalars
# [sampled track elevation points for some distance ahead, e.g. 30 meter ahead, sampled every 1 meter ...
# distance between wheel and track surface ...
# bike speed ...
# suspension travel]
throttle
I assumed this based on the input and output sizes, and the "network_spec” fed to the agent model.
…
…

## Slide 12: First success with tensorForce
Uses default PPO agent from OpenAI gym Cart Pole example.
Env is just the track with single triple jump (i.e. mk_trk1()). Plot show throttle and bike X position vs time.
We can see the trend towards more full throttle, not rolling backwards on jump face. Still some ambiguity with what to do at start. Obviously because it only see 30m ahead, and 30m ahead of start there is nothing. But what's nice about that is we see that as soon as it does see a feature like jump face, high throttle actions predominate.
Reward at ep3000=3.4
Best reward =4.1
Worst reward = approx. -1e6

## Slide 13: First success with tensorForce
Uses default PPO agent from OpenAI gym Cart Pole example.
Env is just the track with single triple jump (i.e. mk_trk1()). Plot show throttle and bike X position vs time.
We can see the trend towards more full throttle, shorter episode time, and monotonic Xpos increase over episode (i.e. no rolling back down jump face)
Reward at ep3000=3.4
Best reward =4.1
Worst reward = approx. -1e6

## Slide 14
Shortened mk_trk1 starting flat section to be closer to agent look ahead distance, and this might be the cause of the almost no learning for that test
Order of figures: Ep3000ep1
Why is this? I think it could be because learning is a stochastic process, due the random element of the explore/exploit process, which means running the same experiment twice will not result in the same learning rate. So maybe this was just a bad experiment in terms of global learning rate (i.e. how much better agent gets over 300 episodes).

## Slide 15
Mk_trk1 in run = 120ft
Order of figures: Ep1->ep3000
Here, global learning rate was slower than for the test on slides 6 & 7
Continue training after stop at ep3000, to ep6000
We can see that here it took about 3500 episodes to achieve similar performance as we saw after only 2000 episodes on slides 6 & 7
Finished episode 2986 after 134 timesteps (reward: -3.2999999999999687)
Finished episode 2987 after 91 timesteps (reward: 1.000000000000016)
Finished episode 2988 after 109 timesteps (reward: -0.7999999999999776)
Finished episode 2989 after 122 timesteps (reward: -2.099999999999973)
Finished episode 2990 after 100 timesteps (reward: 0.10000000000001918)
Finished episode 2991 after 108 timesteps (reward: -0.699999999999978)
Finished episode 2992 after 104 timesteps (reward: -0.2999999999999794)
Finished episode 2993 after 106 timesteps (reward: -0.4999999999999787)
Finished episode 2994 after 184 timesteps (reward: -8.29999999999999)
Finished episode 2995 after 164 timesteps (reward: -6.299999999999962)
Finished episode 2996 after 96 timesteps (reward: 0.5000000000000178)
Finished episode 2997 after 122 timesteps (reward: -2.099999999999973)
Finished episode 2998 after 96 timesteps (reward: 0.5000000000000178)
Finished episode 2999 after 119 timesteps (reward: -1.799999999999974)
Finished episode 3000 after 140 timesteps (reward: -3.8999999999999666)
INFO:tensorflow:Saving checkpoints for 632416 into ./savedTest02/model.ckpt.
Learning finished. Total episodes: 3000. Average reward of last 10 episodes: -2.289999999999977.
cummulative execution time: 3585.5566997528076
Finished episode 5985 after 58 timesteps (reward: 4.300000000000004)
Finished episode 5986 after 59 timesteps (reward: 4.200000000000005)
Finished episode 5987 after 58 timesteps (reward: 4.300000000000004)
Finished episode 5988 after 58 timesteps (reward: 4.300000000000004)
Finished episode 5989 after 59 timesteps (reward: 4.200000000000005)
Finished episode 5990 after 59 timesteps (reward: 4.200000000000005)
Finished episode 5991 after 58 timesteps (reward: 4.300000000000004)
Finished episode 5992 after 58 timesteps (reward: 4.300000000000004)
Finished episode 5993 after 59 timesteps (reward: 4.200000000000005)
Finished episode 5994 after 59 timesteps (reward: 4.200000000000005)
Finished episode 5995 after 59 timesteps (reward: 4.200000000000005)
Finished episode 5996 after 58 timesteps (reward: 4.300000000000004)
Finished episode 5997 after 58 timesteps (reward: 4.300000000000004)
Finished episode 5998 after 58 timesteps (reward: 4.300000000000004)
Finished episode 5999 after 57 timesteps (reward: 4.400000000000004)
Finished episode 6000 after 57 timesteps (reward: 4.400000000000004)
INFO:tensorflow:Saving checkpoints for 858269 into ./savedTest02/model.ckpt.
Learning finished. Total episodes: 6000. Average reward of last 10 episodes: 4.2900000000000045.
cummulative execution time: 1252.185539007187

## Slide 17
4000 episode run with reward model that employed: 1] increased negative step reward for each step after race is longer than shortest time, 2] positive reward at end of episode if new best time was set.

## Slide 18
Added model saving, so that learning sessions can continue from where the last session with same model left off. The results here are from a continuation of the previous 4500 episodes. I then realized that the episode counter needed restart at the last episode from the last session, and updated it. But the issue was that the learner was so good, that it was rarely making better times, so I deleted some of the past TF checkpoints, only to learn that TF doesn’t handle that well, and it started from the beginning again.
Added feature to allow any number of tracks, for a learning session, and for each episode, a track is selected randomly. All race time and best times are track on a per track basis, so we can see full details of the learners progress on each track. Also, for each track, a copy of the environment is constantly updated each time a new best time is set on that track. These env copies are used to draw the race at the end of the session.
What is still not great is that there is no check for if this sessions is a restart, and if so, to load the best times previously set for each track. This is actually important, since we use best time of each track to control the reward signal.
Above: before TF checkpoints was wiped. Below, consecutive 100 ep runs with better plots

## Slide 19
What is still not great is that there is no check for if this sessions is a restart, and if so, to load the best times previously set for each track. This is actually important, since we use best time of each track to control the reward signal.
Above: before TF checkpoints was wiped. Below, consecutive 100 ep runs with better plots

## Slide 20: SubSection for progress of the learner with this neural net. Name=net04
32
20
Input layer:
# state is vector concatenated of vectors and scalars
# [sampled track elevation points for some distance ahead, e.g. 30 meter ahead, sampled every 1 meter ...
# distance between wheel and track surface ...
# bike speed ...
# suspension travel]
throttle
I assumed this based on the input and output sizes, and the "network_spec” fed to the agent model.
8
…
…
…

## Slide 21
network_spec = [
# dict(type='embedding', indices=100, size=32),
# dict(type'flatten'),
dict(type='dense', size=32),
dict(type='dense', size=20),
dict(type='dense', size=8)
]
Race progress for trk1 shown.

## Slide 22
network_spec = [
# dict(type='embedding', indices=100, size=32),
# dict(type'flatten'),
dict(type='dense', size=32),
dict(type='dense', size=20),
dict(type='dense', size=8)
]
Race progress for trk2 shown.

## Slide 23
network_spec = [
# dict(type='embedding', indices=100, size=32),
# dict(type'flatten'),
dict(type='dense', size=32),
dict(type='dense', size=20),
dict(type='dense', size=8)
]
Lack of progression on track1 and 2

## Slide 24
network_spec = [
# dict(type='embedding', indices=100, size=32),
# dict(type'flatten'),
dict(type='dense', size=32),
dict(type='dense', size=20),
dict(type='dense', size=8)
]
Lack of progression on track2. the best time of episode 5000, was 17.5, while the best time after episode 10000 was only slightly shorter.
We must conclude that either the state formulation, the evolution of the reward signal as agent performance improves, or the NN architecture, or some subset of the above items.
I suspect that for trk2, the state is inadequate, to tell the learner about what is ahead, and hence preventing it from making. I think that maybe a non-linear sampling of the track elevation ahead of the bike might work better. E.g. at 1m the sample resolution is 1m, and at 800m, it’s 5m. (800m is the length of redbull straight rhythm track). The outcome is much larger state space.

## Slide 25
Another up to 20000 episodes, we see an interesting change in trk1 performance at 18500ep, where the agent now gets consistently good ace times. Might we be able to say that the agent has “learned” trk1, or overfitted to trk1? Could it have overfitted to trk2 at 10500 before? Whats happening? Whats clear is that the agent is NOT applying its trk1 skills to trk2, despite trk2 having the same first feature (a triple jump)
For the sake of being thorough, I let it run to 15000 episodes and it got a bit better at trk1, and significantly better(~3sec faster) on trk2. at 10500ep. The agent learns something bout trk2, and after demonstrates a noticeable frequency of ~14s races.

## Slide 26
<enter notes for content below>
For the sake of being very thorough, I let it run to 30000 episodes and there was incremental improvement on trk1 for best time, but at ep21000,24000,and28000, we see trk performance consistency drop. I have no idea what might cause that. No improvement on trk2.

## Slide 27: SubSection for progress of the learner with this neural net. Name=net04
53
36
Input layer:
# state is vector concatenated of vectors and scalars
# [sampled track elevation points for some distance ahead, e.g. 30 meter ahead, sampled every 1 meter ...
# distance between wheel and track surface ...
# bike speed ...
# suspension travel]
throttle
I assumed this based on the input and output sizes, and the "network_spec” fed to the agent model.
Input layer (state) is size(53,1), then I just picked 36 and 20 randomly.
20
…
…
…

## Slide 28
<enter notes for content below>
Net04 is not doing as well as net03 on trk1. net04 also seemed to do most of it learning in in the first 200 episodes. At about 4000 episodes, the performance disappears, and the agent just does the same thing until ep6000. why is that, what could possibly result in the agent not doing the explore part of explore/exploit.

## Slide 29
TODO:
Environment:
Create random track generator
  For states ideas 1. below, track maker should define the track feature encoding (i.e. triple jump = 3, flat = 0, table = 1, whoops=9, etc.), and pass this with the trk data. this encoding vector should be a set length so as to be a part of the state. When a track doesn’t have enough features to fill the vector, unused slots are set to -1.
Create whoops section feature
Solver performance
  Check Momentum conservation across change in direction at jump face transition.
  Variable step solver? As bike or wheel acceleration in either X or Y direction goes from [lwr_thr -> upr_thr], time steps goes [dt -> dt/n], where n is positive integer. Still only record data every dt, so run sub-loops at dt/n until a dt size step is complete, then record data
State ideas: Thinking about what mental model a rider would have for the track, these are some state ideas that could work well.
Include a vector which maps out the track features. E.g. 00102040100203, some flat, some flat, a table top, some flat, a double triple jump, some flat, some whoops, etc. this vector encodes the track layout for the agent, so the agent can plan its strategy. A rider would not commit a high fidelity layout to memory, but surely would be able to tell someone the sequence of features from memory.
Have the track profile portion of the state vector be variable length. A minimum length, but if there is a long flat section, the resolution would drop, so seeing further in distance space with same number of sample points. This would help the agent start moving at the beginning for tracks that have a start section that is flat for longer distance than the minimum length. This is sort of attune to how humans look ahead, the more features there are ahead, the less far we look, if there are few or no feature in the near distance, we sort of turn our focus away from that, and look far ahead, with poor resolution, to see what features we can.
I think that maybe a non-linear sampling of the track elevation ahead of the bike might work better. E.g. at 1m the sample resolution is 1m, and at 800m, it’s 5m. (800m is the length of redbull straight rhythm track). The outcome is much larger state space.
Agent and hyper parameters
Setup multi-treading
Setup Bayesian optimization
Model architecture
  Add drop out. Will this be helpful in this context?